## Slide 1
DGIST
Team Project Proposal:
Cache Partitioning &Write-Scheduling in Demand-based FTL
201842003 Junsu Im
201822020 Jinwook Bae
Data-Intensive Computing Systems Laboratory(DataLab), DGIST
Real-time Embedded Systems (IC616)

## Slide 2: Index
Introduction
Background
Motivation
PTSD
Future Work
DGIST

## Slide 3: Index
Introduction
Background
Motivation
PTSD
Future Work
DGIST

## Slide 4: Introduction
Real-time apps need to store, retrieve and process large volume of sensor data
  Unmanned Aerial Vehicles(UAVs)
  Autonomous Cars
Because of lack of the system memory, the file I/Os are occur
To satisfy Real Time processing, the File I/O should be predictable.
  read operations can’t be handled as asynchronous way, it is more important than write operations.
DGIST

## Slide 5: Introduction
SSD instead of HDD must be adopted to meet requirements of real-time systems
  Fast access time
  Shock resistance
  Low power consumption
However, For SSDs, DRAM is required in proportion to the size of storage
  to store massive data generated from sensors, more memory is needed
Why SSD need DRAM?
  Logical to Physical address mapping
DGIST

## Slide 6: Index
Introduction
Background
Motivation
PTSD
Future Work
DGIST

## Slide 7: Background
DGIST
a
b
c
d
e
f
g
h
i
j
a
b
c
d
a’
b’
c’
e
f
g
h
i
0
1
2
3
4
5
6
7
8
9
10
11
0
1
2
3
4
5
6
7
8
9
10
11
0 | 4
1 | 5
2 | 6
3 | 3
4 | 
5 | 
6 | 7
7 | 8
8 | 9
9 | 10
10 | 11
11 | 
LPA
PPA
LPA
PPA
a’
b’
c’
?
Address Mapping

## Slide 8: Background
DGIST
d
j
12
13
14
15
a
b
c
d
e
f
g
h
i
j
a
b
c
d
a’
b’
c’
e
f
g
h
i
0
1
2
3
4
5
6
7
8
9
10
11
0
1
2
3
4
5
6
7
8
9
10
11
LPA
PPA
a’
b’
c’
Garbage Collection
Over-Provisioning
Block Erase!

## Slide 9: Index
Introduction
Background
Motivation
PTSD
Future Work
DGIST

## Slide 10: Motivation
  Hybrid, Block mapping can guarantee read response time in some case, but it cause a lot of additional writes.
  Demand Page Mapping’s write operation is quite similar to optimal, but it can’t guarantee read in many cases.
    Similar to demand paging in virtual memory
  Page mapping is not adoptable in embedded system because of memory usage.
DGIST
 | Write Amplification Factor | Read Latency | Memory Usage
Hybrid Mapping | Over 10x | Partially Guarantee | Middle, variable size
Block Mapping | Over 30x | Partially Guarantee | Very low, fixed size
Demand Page Mapping | Over 2x | Rarely Guarantee | Middle, variable size
Page Mapping | Optimal | Optimal | Very high, fixed size

## Slide 11: Motivation
DGIST
Cache Hit
Clean Eviction
Dirty Eviction + GC

## Slide 12: Index
Introduction
Background
Motivation
PTSD
  Cache Partitioning
  I/O Scheduling
  Write Optimizing
Future Work
DGIST

## Slide 13: PTSD
PTSD:cache ParTitioning and I/O-Scheduling in Demand-based FTL
  Mapping cache for reads and writes are partitioned into two regions
  Remove dirty eviction from read I/O path
  Protect reads from write disturbance by I/O scheduling
Main functionalities
  Cache Partitioning
  I/O scheduling
  Write optimizing
DGIST

## Slide 14: PTSD
Experiments
  I/O performance is tested in mixed workload(R/W 5:5) after filling device
    Sequential Write + Mixed Random Read/Write
  Each FTL and Functionality is implemented as C program in userspace
  We evaluated on the embedded board which is simulating the SSD
    Xilinx ZCU 102
    512GB Capacity
    4GB DRAM
    4 1GHz ARM Cores
DGIST

## Slide 15: PTSD
Cache Partitioning
Cache Partitioning
  Separate Clean/Dirty cache
  Only clean eviction occurs on read
  Dirty evictions are all imputed to write
  Cache utilization could be a drawback
DGIST
Dirty eviction…
Dirty eviction…
Clean eviction…
Clean eviction…
Dirty eviction…
Dirty eviction…
Clean eviction…
Clean eviction…
Read
Write
Read
Write

## Slide 16: PTSD
Cache Partitioning
DGIST
Good average latency!
Tail latency still exists…
Block by writes?
Context switch?

## Slide 17: PTSD
​I/O Scheduling
  force writes to stop when reads are waiting
  Writes are flushed only when the read I/O queue is empty
  After flush, we clean the device until write requests are finished
DGIST

## Slide 18: PTSD
​I/O Scheduling
DGIST
Good Tail Latency!

## Slide 19: PTSD
​I/O Scheduling
DGIST

## Slide 20: PTSD
Write Optimizing
  Same mapping granularity in both cache is inefficient
    In dirty cache, the clean entry in dirty page can occupy the cache memory
  Also this effect more affect to write performance degrading with cache partitioning and I/O scheduling
DGIST

## Slide 21: PTSD
Write Optimizing
DGIST

## Slide 22: Index
Introduction
Background
Motivation
PTSD
Future Work
DGIST

## Slide 23: Future work
Limitation of I/O scheduling
  we just force to stop write services at software level, rather than hardware support
  This approach hides read tail latency to write requests
  If software I/O queue is overflowed out of limited queue depth, reads are delayed by writes in the end
Adaptive partitioning
  we expect that the optimal partitioning point for given workload is exists
  adaptive partitioning by detecting workload in runtime would be effective to meet requirements adjustably
DGIST

## Slide 24
Q & A
DGIST